# SPI configuration port
A write or read operation is initiated by pulling spi_ncs low. There are two parts to a communication cycle with the FPGA. In the first part, a 8-bit instruction word is written to the FPGA, coincident with the first 8 spi_sclk rising edges. The instruction word provides information regarding the data transfer, which is the second part of the communication cycle. The instruction word defines whether the upcoming data transfer is a read or a write and the starting register address for the first word of the data transfer.

7	6	5	4	3	2	1	0
R/W	ADDR

## Setting a register value
If the instruction word is for a write operation, the next 32 spi_sclk cycles clock in data for the address specified in the instruction word. Data bits are registered on the rising edge of spi_sclk.

## Reading a register value
If the instruction word is for a read operation, the next 32 SCLK cycles clock out the data from the address specified in the instruction word. The readback data is updated on the falling edge of spi_sclk.

# Register set description
## Register 0x00
Identification
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
MAGIC
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
MAGIC

MAGIC	[31..0]	R	Magic Identifier / 32 bit unsigned integer / The magic value can be used to detect is the FPGA is running and the communication interface is working. It always reads 0xDEADBEEF at the moment.

## Register 0x01
PWM #1
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
DUTY
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
FREQ

FREQ	[15..0]	R/W	PWM1 Frequency / 16 bit unsigned integer / The frequency of the first PWM output is configured vis this value: / PWM_freq = left({ {80 MHz} OVER {FREQ+1} }right)
DUTY	[31..0]	R/W	PWM1 Duty Cycle / 16 bit unsigned integer / The duty cycle of the first PWM output is configured vis this value: / PWM_duty = left({ {DUTY} OVER {FREQ+1} }right)

## Register 0x02
PWM #2
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
DUTY
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
FREQ

FREQ	[15..0]	R/W	PWM1 Frequency / 16 bit unsigned integer / The frequency of the second PWM output is configured vis this value: / PWM_freq = left({ {80 MHz} OVER {FREQ+1} }right)
DUTY	[31..0]	R/W	PWM1 Duty Cycle / 16 bit unsigned integer / The duty cycle of the second PWM output is configured vis this value: / PWM_duty = left({ {DUTY} OVER {FREQ+1} }right)

## Register 0x03
ADC Timing
31	30	29	28	27	26	25	24		23		22	21	20	19	18	17	16

15	14	13	12	11	10	9		8	7		6	5	4	3	2	1	0
ACQLEN										CLKDIV

CLKDIV	[7..0]	R/W	AD7357 SCK Frequency / 8 bit unsigned integer / The frequency of the SCK line to the AD7357 ADC is configured via this value: / F_SCK = left({ {80 MHz} OVER {CLKDIV} }right)
DUTY	[15..8]	R/W	AD7357 Acquisition Time / 8 bit unsigned integer / Number of SCK cycles the CS Line to the AD7357 is held high between two conversions.

## Register 0x04
SSC Interface
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16

15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
CLKDIV																TM

TM	[0]	R/W	Testmode / Decides if the testmode of the SSC Interface is enabled: / 0 normal operation / 1 testmode enabled, data is replaced by a 16 bit counter
CLKDIV	[15..8]	R/W	SSC Clock Frequency / 8 bit unsigned integer / The frequency of the Clock line of the SSC interface to the MCU is configured via this value: / F_SSC = left({ {80 MHz} OVER {2 cdot (CLKDIV+1)} }right)

## Register 0x06
Decimation Filter
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16

15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
														RATE

RATE	[2..0]	R/W	Decimation Factor / Configures the decimation factor of the filter: / 000 no decimation / 001 Samplerate is reduced by factor 2 / 010 Samplerate is reduced by factor 4 / 011 Samplerate is reduced by factor 8 / 100 Samplerate is reduced by factor 16 / 101 Samplerate is reduced by factor 32 / 110 Samplerate is reduced by factor 64

## Register 0x09
ADC Channel Swap
31	30	29	28	27	26	25	24	23	22	21	20	19	18	17	16

15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
															SWAP

SWAP	[0]	R/W	Channel Swap / Decides if the ADC channels get swapped: / 0 normal operation matrix{I_swap # "= I" ## Q_swap # "= Q"} / 1 inverted spectrum matrix{I_swap # "= Q" ## Q_swap # "= I"}

## Register 0x08
ADC Sample Gain
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
GAIN_Q
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
GAIN_I

GAIN_I	[15..0]	R/W	Gain (I-Channel) / 16 bit unsigned integer / Each I sample is scaled with the value of GAIN_I: / I_scaled = left({ {I_swap cdot "GAIN_I"} OVER 32768 }right)
GAIN_Q	[31..0]	R/W	Gain (Q-Channel) / 16 bit unsigned integer / Each Q sample is scaled with the value of GAIN_Q: / Q_scaled = left({ {Q_swap cdot "GAIN_Q"} OVER 32768 }right)

## Register 0x07
ADC Sample Offset
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
OFF_Q
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
OFF_I

OFF_I	[15..0]	R/W	Offset (I-Channel) / 16 bit signed integer / The value off OFF_I is added to each I sample: / I_out = I_scaled + "OFF_I"
OFF_Q	[31..0]	R/W	Offset (Q-Channel) / 16 bit signed integer / The value off OFF_Q is added to each Q sample: / Q_out = Q_scaled + "OFF_Q"

## Register 0x0A - 0x0C
0x0A - GPIO – Output Enable
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
					GPIO_OE

0x0B - GPIO – Output Data
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
					GPIO_OD

0x0C - GPIO – Input Data
15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
					GPIO_ID

GPIO_OE	[10..0]	R/W	Output Enable / Sets the direction of the GPIO Pin: / 0 GPIO is input / 1 GPIO is output
GPIO_OD	[10..0]	R/W	Output Data / Sets the data written on the Output driver: (only relevant if the corresponding GPIO_OE Bit is set) / 0 GPIO is driven low / 1 GPIO is driven high
GPIO_ID	[10..0]	R	Input Data / Gets the data read from the Input driver: / 0 GPIO is low / 1 GPIO is high

GPIO Mapping:
- GPIO[0:9]:	A[1-10] Pin
- GPIO[10]:	FPGA LED
## Register 0x0D
Reference Frequency Measurement
31	30	29	28	27	26	25	24		23	22	21	20	19	18	17	16
REF_UPD								REF_CNT
15	14	13	12	11	10	9		8	7	6	5	4	3	2	1	0
REF_CNT

REF_CNT	[24..0]	R	Reference Counter / Return the number of the CLKPO (typical 30MHz) Cycles between the last two rising edges on the 1PPS Signal.
REF_UPD	[31:25]	R	Reference Update Counter / This 7 Bit Counter is incremented every time a new value is latched into the REF_CNT register.